## Slide 1
Safe Lane Selection
Camera-based lane perception, obstacle assignment, and explainable control
Samuele Moranzoni · Ferdinando Giordano
Aim: identify the ego-lane, estimate orientation, detect obstacles through camera perception, and test a safe path using a simple geometric pipeline.
Insert final top-down / lane-debug screenshot
8 min presentation structure

## Slide 2
MOTIVATION
Why We Simplified The Problem
Previous version mixed many concerns: multi-lane logic, world-pose control, ToF stop, markers, obstacle logic, and several control states.
Main issue: perception and control were hard to debug and hard to explain mathematically.
Improvement: isolate the core perception problem in a clean 2-lane road with 3 stable lane boundaries.
Result: stable line detection, explainable geometry, and measurable debug quantities.
Key message: simplifying the scene was not removing the problem; it made the geometry observable and testable.
Insert before/after setup image

## Slide 3
PERCEPTION CORE
Line Geometry From The Camera Image
The RoboMaster front camera observes white lane boundaries on a black road.
Lane pixels are segmented, edges are extracted, and Hough transform returns line segments.
Each Hough segment gives two image points, which define one line model.
We represent lane lines as x = m*y + b because they are almost vertical in the image.
Line model
Given two points: (x_a, y_a), (x_b, y_b)
m = (x_b - x_a) / (y_b - y_a)
b = x_a - m*y_a
L(y) = m*y + b
Insert lane-debug image with Hough lines
Important: the lookahead intersections x1, x2, x3 do not define the lines; they are computed after the line equations are known.

## Slide 4
PROJECTIVE GEOMETRY
Vanishing Point And Orientation
Parallel road boundaries converge in the image due to perspective projection.
The intersection of lane boundary lines estimates the vanishing point.
If the vanishing point lies on the image center, the robot is aligned with the road direction.
A horizontal shift of the vanishing point indicates heading/orientation error.
Vanishing point error
VP = intersection(L_i, L_j)
heading_error_px = VP_x - c_x
heading_error_norm = (VP_x - c_x) / width
Angle approximation
f_x = width / (2*tan(FOV_x/2))
theta = atan((VP_x - c_x) / f_x)
with width=640, FOV_x=90 deg:
f_x = 320 px
The angle is used for interpretation/debug; the controller can still use the normalized error for robustness.

## Slide 5
LANE SELECTION
Ego-Lane Identification
A fixed lookahead row is selected near the lower part of the image.
The three lane boundaries are evaluated at that row.
The image center tells which visible lane currently contains the robot.
The lane center gives the lateral error used by the controller.
Lane intervals
x1 = L1(lookahead_y)
x2 = L2(lookahead_y)
x3 = L3(lookahead_y)
left_lane = [x1, x2]
right_lane = [x2, x3]
Lane center error
left_center = (x1 + x2) / 2
right_center = (x2 + x3) / 2
lateral_error = selected_center - c_x
lateral_error_norm = lateral_error / width
Insert screenshot with x1, x2, x3 and lane centers

## Slide 6
COLOR PERCEPTION
Obstacle Detection And Lane Assignment
Red and green obstacle vehicles are segmented in HSV color space.
Contours provide a bounding box around the strongest colored blob.
The obstacle is represented by the bottom-center point of the box.
Lane assignment uses the lane boundary equations at the obstacle bottom_y.
Obstacle point
bbox = (x, y, w, h)
obstacle_x = x + w/2
obstacle_y = y + h
Lane assignment
x1 = L1(obstacle_y)
x2 = L2(obstacle_y)
x3 = L3(obstacle_y)
if x1 <= obstacle_x <= x2: lane = left
if x2 <= obstacle_x <= x3: lane = right
The obstacle does not need its own line equation. It is classified using the already estimated lane geometry.

## Slide 7
ARCHITECTURE
ROS 2 Implementation
Node graph
/rm0/camera/image_color
-> lane_perception_node
publishes /lane_geometry
/rm0/camera/image_color + /lane_geometry
-> obstacle_perception_node
publishes /obstacle_detection
/lane_geometry + /obstacle_detection
-> lane_controller_node
publishes /rm0/cmd_vel
Perception nodes are independent from the control loop.
The controller runs at a fixed rate and uses the latest valid geometry.
If an obstacle is close and in the current lane, the controller targets the other lane.
This keeps the behavior explainable and testable topic-by-topic.
Insert ROS graph / terminal topics

## Slide 8
EXPLAINABILITY
Debug Visualization And Results
lane_debug/image: Hough lines, selected boundaries, vanishing point, lane centers, lateral error, and heading angle.
obstacle_debug/image: obstacle bbox, color, lane assignment, close flag, center point, and bbox coordinates.
top-down camera: observer-only view for validation and demo video; it is not used by the robot perception pipeline.
Outcome: stable two-lane detection and a clear explanation of each robot decision.
Insert lane debug screenshot
Insert obstacle debug screenshot
Insert top-down demo screenshot